## Slide 1
Homework 4 (Due: 5/24)
(1) Write a Matlab or Python program to measure the structural similarity (SSIM) of two images A and B. The sizes of A and B are equivalent.
SSIM(A, B, c1, c2)
where c1 and c2 are some adjust constants.
The Matlab or Python code should be handed out by NTUCool. (20 scores)

## Slide 2
(2) (a) How do we use three real multiplications to implement a complex multiplication? (10 scores)
(b) Suppose that
How do we implement above matrix operation with the least number of real multiplications? (10 scores)
根據講義 p.349，
  => 總共需要 3 MULs, 5 ADDs

## Slide 3
(b)
=> 總共 10 MULs

## Slide 4
(3) Determining the numbers of real multiplications for the (a) 125-point DFT,
(b) the 147-point DFT, and (c) the 385-point DFT. (15 scores)
125 = 5 x 25，使用 case2:
  N = P1 x P2，5-point DFT 的乘法量為 10，25-point DFT 的乘法量為 148，有 24*4 個值不為 125/12 及 125/8 的倍數，則 125-point DFT 的乘法量為 25*10 + 5*148 + 3*24*4 = 1278。
147 = 3 x 49
  49 = 7 x 7，使用 case2:
  7-point DFT 的乘法量為16，則 49-point DFT 的乘法量為 7*16 + 7*16 + 3*6*6 = 332。
  再使用 case1:
  3-point DFT 的乘法量為 2，49-point DFT 的乘法量為 332，則 147-point DFT 的乘法量為 49*2 + 3*332 = 1094。
385 = 11 x 35，使用 case1:
  11-point DFT 的乘法量為 40， 35-point DFT 的乘法量為 150，則 385-point DFT 的乘法量為 35*40 + 11*150 = 3050 。

## Slide 5
(4) What is the complexity of the 3D DFT as follows? Express the solution in terms of the big order. (10 scores)

## Slide 6
(5) Suppose that there are 1200 cars in a dataset and an algorithm detects 1000 cars. However, among the detected cars, 100 of them are in fact other objects. Determine the precision, the recall, and the F-score of the algorithm.
(10 scores)

## Slide 7
(6) Suppose that length(x[n]) = 1100. What is the best way to implement the convolution of x[n] and y[n] if
(a) length(y[n]) = 500, (b) length(y[n]) = 40,
(c) length(y[n]) = 6, and (d) length(y[n]) = 2 ? (25 scores)
Please show (i) the convolution method (direct, sectioned convolution, or non-sectioned convolution), (ii) the number of points of the FFT, (iii) and the number of real multiplications for the best implementation method. Also, consider the general case where x[n] and y[n] are complex sequences and the FFT of y[n] can be computed in prior.

## Slide 8
(Extra): Answer the questions according to your student ID number.
(ended with (2, 7), (3, 8), (4, 9), (0, 5))