## Slide 1
Homework 2 (Due: 4/12)
(1) Write a Matlab or Python code that uses the frequency sampling method to design a (2k+1)-point discrete differentiation filter H(F) = j2πF when -0.5 < F < 0.5 (k is an input parameter and can be any integer). (25 scores)
The transition band is assigned to reduce the error (unnecessary to optimize). (i) The impulse response and (ii) the imaginary part of the frequency response (DTFT of r[n], see pages 113 and 114) of the designed filter should be shown. The code should be handed out by NTU Cool.

## Slide 2
impulse response
the imaginary part of the frequency response
(ii)
(i)

## Slide 3
(2) Can the techniques of the weight function and the transition band be applied in the FIR filter designed by (a) the MSE method and (b) the frequency sampling method? Why? (10 scores)
(a)
weight function 可以於 MSE，如同 p.87 所示，
transition band 也可以用於 MSE，只需要將 transition band 的範圍和的 weight 視為 0，如同 p.89 所示。
(b)
weight function 無法用於 frequency sampling，因為 frequency sampling 是取樣之後直接做 ifft，沒有辦法用到 weight function 。
transition band 可以用於 frequency sampling，透過調整 sample 點的位置來設定 transition band 。

## Slide 4
(3) Suppose that the smooth filter is h[n] = a for |n| ≦ 5, h[n] = 0.023 for 6 ≦ |n| ≦ 10, and h[n] = 0 otherwise. (a) What is the value of a? (b) What is the efficient way to implement the convolution y[n] = x[n] * h[n]? (10 scores)
(a)
(b)
h[n] 可以拆解成 加上 這兩段，而 經過 Z transform 為

## Slide 5
(4) The following figures are the impulse responses of some filters. Which one is a suitable smoother when we want to extract (a) small scaled features? (b) large scaled features? Also illustrate the reasons. (10 scores)
(i)
(ii)
(iii)
(iv)
Smoother 通常會是 even 對稱且 與 較為符合 。
(a)
要 extract 比較小的範圍則 smoother 的寬度要窄一些，獲得的資訊才會是比較少的， 較為合適。
(b)
要 extract 比較大的範圍則 smoother 的寬度要寬一些，拿可以拿取比較多的資訊， 較為合適。

## Slide 6
(5) If the z-transform of h[n] is
(b) Convert the IIR filter into the minimum phase filter.
(20 scores)
(a) Determine the cepstrum of h[n].
(Hint: z = 2-0.5 is one of the zeros of H(z))
(a)

## Slide 7
(5) If the z-transform of h[n] is
(b) Convert the IIR filter into the minimum phase filter.
(20 scores)
(a) Determine the cepstrum of h[n].
(Hint: z = 2-0.5 is one of the zeros of H(z))
(b)

## Slide 8
(6) Suppose that the cepstrum of a signal x[n] is
Determine x[n] using the Z transform and exp( ). (10 scores)

## Slide 9
(7) (a) What are the two main advantages of the minimum phase filter? (b) In addition to time-frequency analysis, what are two main applications of the Hilbert transform? (c) Compared to the equalizer, what are the two main advantages of the cepstrum to deal with the multipath problem? (15 scores)
(a)
(b)
(c)

## Slide 10
(Extra): Answer the questions according to your student ID number.
(ended with (4, 9), (0, 5), (1, 6), (2, 7))