## Slide 1
Homework 1 (Due: March 22nd)
(1) Design a Mini-max highpass FIR filter such that (40 scores)
 Filter length = 21,  Sampling frequency fs = 8000Hz,
 Pass Band 1800~4000Hz  Transition band: 1600~2000 Hz,
 Weighting function: W(F) = 1 for passband, W(F) = 0.8 for stop band .
 Set  = 0.0001 in Step 5.
Show (a) the frequency response, (b) the impulse response h[n], and
(c) the maximal error for each iteration.
0 Hz
1600 Hz
1800 Hz
2000 Hz
※ The code should be handed out by NTUCool, too.

## Slide 2
the frequency response
(b) the impulse response h[n]
(c) the maximal error for each iteration.

## Slide 3
(2) (a) Which type of systems can be implemented by convolution?
(b) How do we convert convolution into an addition operation? (10 scores)
Linear time-invariant systems.
  對於 LTI system，符合以下兩點：
  Linear(Scaling + Superposition)：
  給予 input x1(t) 得到 output y1(t)，給予 input x2(t) 得到 output y2(t)，則給予 input ax1(t)+bx2(t) 會得到 output 為 ay1(t)+by2(t)。
  Time-invariant：
  給予 input x(t) 得到 output y(t)，則給予 input x(t-s) 會得到 output為 y(t-s)。
  若 input 為 Impulse function (t) 而 output 為 Impulse response h(t)，我們可以先將 input x(t) 變成由 Impulse function (t) 所組成的式子： ，則 output y(t) 會得到 。
  這就等於 x(t) 與 h(t) 做 convolution。
在 time domain 若為 convolution，經過 Fourier transform 可轉為相乘，再兩邊取 log 就可以變成 addition operation。

## Slide 4
(3) (a) Describe three advantages of the FIR filter.
(b) How do we implement y[n] = x[n] *(0.7nu[n]+ 0.2nu[n]) using the recursive method where * means the convolution and u[n] is the unit step function?
(10 scores)
1. Output has finite length.
  2. Usually less computation loading.
  3. Stable. Because output is a sum of finite number of the input.
Do z transform.
  Do inverse z transform.

## Slide 5
(4) What are the roles of (a) the transition band and (b) the weight function for minimax FIR filter design? (10 scores)
(a)
在不增加濾波器的點數的情況下，transition band可以讓誤差減少。 transition band越寬，設計出來的濾波器就相對平緩，passband 和 stopband的誤差就可以變小。有transition band的話，才有機會讓誤差<0.5。
(b)
可以透過給予passband 和stopband不同加權，在特定頻帶規定誤差要比較小， weight 就給大一點，在某些頻帶誤差允許大一些， weight就給小一點。

## Slide 6
(5) Suppose that x[n] = y(0.001n) and the length of x[n] is 6000. If X[m] is the FFT of x[n], determine m such that X[m] correspond to the frequencies of (a) 200Hz and (b) -100Hz. (10 scores)

## Slide 7
(6) Use the MSE method to design the 7-point FIR filter that approximates the band filter of Hd(F) = 1 for 0.1 < |F| < 0.4 and Hd(F) = 0 for |F| < 0.1 or |F| >0.4.
(10 scores)

## Slide 8
(7) Estimate the length of the digital filter if both the passband ripple and the stopband ripple are smaller than 0.01, the sampling interval Δt = 0.0001, and the transition band is from 3000Hz to 3300Hz. (10 scores)

## Slide 9
(Extra): Answer the questions according to your student ID number.
(ended with 0, 1, 2, 3, 5, 6, 7, 8)
Q: