## Slide 1
Homework 3 (Due: May 3rd)
Write a Matlab or Python code for the 4:2:0 image compression technique.
B = C420(A), A is the input color image and B is the reconstructed image.
Just use the interpolation method for reconstruction. The code should be handed out by NTUCool. (Note: The command rgb2ycbcr cannot be used.)
(25 scores)

## Slide 2
(2) Suppose that there is a multipath system y[n] = x[n] + 0.3x[n-15] + 0.2x[n-25]. (a) Find p[n] such that y[n] = x[n] * p[n]. (b) Design the lifter to remove the effect of p[n] and try to not destroy x[n] as possible. (10 scores)
根據講義 p.193， ，
Filtering out the echo by the following “lifter”:

## Slide 3
(3) Suppose that there are three vocal signals: (i) cos(300t), (ii) -sin(1200t), (iii) sin(6000t). (a) Which voice sounds louder? (b) Which voice signal can be propagated to a longest distance? (10 scores)
頻率：
(i) , (ii) , (iii)
(iii)>(ii)>(i)
波長：
(i)>(ii)>(iii)
在頻率小於 3000HZ 的情況下，頻率越高人耳聽到聲音所需要的分貝數就越低，(iii)的頻率最大，所以人耳聽到 (iii) 的聲音是最大的。
波長越長 => 傳播距離較遠，(i)的波長最大，所以 (i) 傳播的距離最遠。

## Slide 4
(4) Suppose that for a stringed instrument the frequency of Do is 240 Hz. (a) Determine the frequencies of Mi and So for the instrument. (b) Suppose that the rate of wave propagation is 340m/sec. Determine the lengths of the strings to generate Mi and So for the stringed instrument. (10 scores)
根據講義 p.240，
Mi 和 Do 差 4 個半音，
So 和 Do 差 7 個半音，

## Slide 5
(5) In addition to the DCT, which is adopted by MP3, write at least three possible ways that can compress a music signal more efficiently. (10 scores)
能量只集中在某些特定區域，例如：HZ…，只要記錄這些地方，其他地方可以精簡。
在同一個音當中頻率是穩定的。
Repeated melody，大部分的音樂旋律都會重複。

## Slide 6
(6) In the JPEG process, (a) why the DCT is used instead of the DFT for transformation? Write at least two reasons. (b) Why the input image is separated into several 8x8 blocks before using the DCT? Write at least two reasons. (c) Why the DC difference is encoded instead of the original DC value? (d) Why zigzag is beneficial for AC term encoding? (20 scores)
D

## Slide 7
(7) Suppose that P(x = n) = en/(n!) for n = 0, 1, 2, 3….., 40 where  = 0.97. Also suppose that length(x) = 50000. Estimate the range of the total coding lengths in the binary system when using (i) the Huffman code and (ii) the arithmetic code. (15 scores)

## Slide 8
(Extra): Answer the questions according to your student ID number.
(ended with 0, 1, 3, 4, 5, 6, 8, 9)